Names____________________

# BA 353: OCAs 11 and 12 Key

1) For an inventory control system with annual demand of 50,000 units, holding cost of $5 and setup cost/delivery charge of $200, lead time of 3 days and open 365 days per year, calculate:

- Q* = sqrt (2*50000*200/5) = 2000 units

- IC = 50000/2000*200 + 5*2000/2 = $10,000

- How many deliveries per year? 50000/2000 = 25

- What is average inventory? 2000/2 = 1000 units

- What is the ROP? Around 50000/365*3 = 411 units.

2) Demand for gasoline at a local gas station is constant at about 800 gallons per day.  The gas station is open every day of the year.  Assume that the purchase price per gallon is $1.70 and that the annual holding cost of a gallon of gas is about $0.85.  Every time a tanker makes a delivery, there is a $250 delivery charge charged to the station.

a) How much gasoline does the gas station sell annually?  292,000

b) Calculate the EOQ = sqrt (2*292000*250/0.85) =13,100 and the number of annual deliveries. -= 292000/13100 ≈ 23

c) Determine the TC. 1.7*292000 + 292000/13100*250 + 0.85*13100/2 = $507,500

d) Assume that the tanker holds up to 30,000 gallons.  If the gas station orders a full tanker of gasoline, they do not have to pay the delivery charge.  Is it more cost-effective to continue following the EOQ policy or to begin ordering full tankers for every delivery?  What is the difference in total cost?  Cost actually goes up to ~$509,000, save $1500 sticking with EOQ.

TC = 1.7*292000 + 0 + 0.85*30000/2 = $509,000

3) Monthly (careful, I may be tricking you here) demand for a product is approximately 1000 units.  The setup/ordering cost is $1000 and the annual holding cost is 30% of the purchase price.  The purchase price depends on the order quantity, as listed in the table below.  Determine the optimal order quantity that minimizes TC, the total annual cost.

| Order Quantity | Purchase Price | Q* | Effective Q | TC |
| --- | --- | --- | --- | --- |
| Q < 2000 | $50.00 | 1265 | 1265 | $619k |
| 2000 ≤ Q < 5000 | $49.50 | 1271 | 2000 | $615k |
| Q ≥ 5000 | $49.00 | 1278 | 5000 | $627k |

Extra Credit 1) For the data in problem A) of the EOQ handout, graph and print the function IC = S*(D/Q) + H*(Q/2), where IC is the y-variable and Q is the x-variable, between Q = 100 and Q =2000.  (Use Excel and draw a Scatter diagram.  Note: you can adjust the scale on the y-axis to make the minimum point more obvious.)  Is the minimum cost where you would expect it to be, given the EOQ from problem A)?

Looks like a Nike swoosh.

Extra Credit 2) Graph and print the TC as a function of Q from Q = 1000 to Q = 6000 for problem 3).